Q. 1 – Q. 25 carry one mark each.

Q.1

The current ib through the base of a silicon npn transistor is

mA)

10000

(cos1.01

t





. At 300 K,

the rin the small signal model of the transistor is

ib

r

r

B

C

E

(A) 250 Ω

(B) 27.5 Ω

(C) 25 Ω

(D) 22.5 Ω

Q.2

The power spectral density of a real process X(t) for positive frequencies is shown below. The

values of E[X2(t)] and )]([

tXE , respectively, are

SX(ω)

400 (-104)

ω (103 rad/s)

10 11

9

6

0

(A) 6000/π, 0

(B) 6400/π, 0

(C) 6400/π,

)2

/(20

(D) 6000/π,

)2

/(20

Q.3

In a baseband communications link, frequencies upto 3500 Hz are used for signaling. Using a

raised cosine pulse with 75% excess bandwidth and for no inter-symbol interference, the maximum

possible signaling rate in symbols per second is

(A) 1750

(B) 2625

(C) 4000

(D) 5250

Q.4

A plane wave propagating in air with

V/m

)

ˆ

5

ˆ

6

ˆ

8(

)4

3

(

y

xtj

z

y

x

ea

a

a

E













о

is incident on a

perfectly conducting slab positioned at

0

≤

x

. The E

о

field of the reflected wave is

(A)

V/m

)

ˆ

5

ˆ

6

ˆ

8(

)4

3

(

y

xtj

z

y

x

ea

a

a













(B)

V/m

)

ˆ

5

ˆ

6

ˆ

8(

)4

3

(

y

xtj

z

y

x

ea

a

a













(C)

V/m

)

ˆ

5

ˆ

6

ˆ

8(

)4

3

(

y

xtj

z

y

x

ea

a

a













(D)

V/m

)

ˆ

5

ˆ

6

ˆ

8(

)4

3

(

y

xtj

z

y

x

ea

a

a













Q.5

The electric field of a uniform plane electromagnetic wave in free space, along the positive

x direction, is given by



xj

z

y

eaj

a

E

25

ˆ

ˆ

10







о

. The frequency and polarization of the wave,

respectively, are

(A) 1.2 GHz and left circular

(B) 4 Hz and left circular

(C) 1.2 GHz and right circular

(D) 4 Hz and right circular

Page 3

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

3/20

Q.6

Consider the given circuit.

A

B

CLK

In this circuit, the race around

(A) does not occur

(B) occurs when CLK = 0

(C) occurs when CLK = 1 and A = B = 1

(D) occurs when CLK = 1 and A = B = 0

Q.7

The output Y of a 2-bit comparator is logic 1 whenever the 2-bit input A is greater than the 2-bit

input B. The number of combinations for which the output is logic 1, is

(A) 4

(B) 6

(C) 8

(D) 10

Q.8

The i-v characteristics of the diode in the circuit given below are

│

⎩

│

⎨

⎧



≥





V7.0

,A0

V7.0

,A

500

7.0

v

v

v

i

+

1kΩ

10V

-

i

+

-

v

The current in the circuit is

(A) 10 mA

(B) 9.3 mA

(C) 6.67 mA

(D) 6.2 mA

Q.9

In the following figure, C1 and C2 are ideal capacitors. C1 has been charged to 12 V before the ideal

switch S is closed at t = 0. The current i(t) for all t is

C1

t = 0

C2

i(t)

S

(A) zero

(B) a step function

(C) an exponentially decaying function

(D) an impulse function

Q.10 The average power delivered to an impedance

)3

4( j



Ωby a current

)100

100(cos5 

t



A is

(A) 44.2 W

(B) 50 W

(C) 62.5 W

(D) 125 W

Q.11 The unilateral Laplace transform of f (t) is

1

1

2





ss

. The unilateral Laplace transform of

)(

tft is

(A)

2

2

)1

(







ss

s

(B)

2

2

)1

(

12









s

s

s

(C)

2

2

)1

(



s

s

s

(D)

2

2

)1

(

12







s

s

s

Page 4

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

4/20

Q.12 With initial condition 5.0)1(



x

, the solution of the differential equation,

tx

dt

dx

t





is

(A)

2

1





tx

(B)

2

1

2 



tx

(C)

2

2

t

x 

(D)

2

t

x 

Q.13 The diodes and capacitors in the circuit shown are ideal. The voltage v(t) across the diode D1 is

v(t)

cos(t)

+

-

D2

C1

C2

D1

(A) 1)(cos



t



(B) )(sint



(C)

)(cos

1

t





(D)

)(sin

1

t





Q.14 In the circuit shown

5 Volts

A

A

B

B

C

C

Y

(A) CBAY





(B)

CBA

Y

)

( 



(C)

CBA

Y

)

( 



(D) CBAY





Q.15 A source alphabet consists of N symbols with the probability of the first two symbols being the

same. A source encoder increases the probability of the first symbol by a small amount and

decreases that of the second by . After encoding, the entropy of the source

(A) increases

(B) remains the same

(C) increases only if N = 2

(D) decreases

Q.16 A coaxial cable with an inner diameter of 1 mm and outer diameter of 2.4 mm is filled with a

dielectric of relative permittivity 10.89. Given

mH

10

4

7

0









,

mF

36

10 9

0









, the

characteristic impedance of the cable is

(A) 330 Ω

(B) 100 Ω

(C) 143.3 Ω

(D) 43.4 Ω

Q.17 The radiation pattern of an antenna in spherical co-ordinates is given by





4

cos

)( 

F

;

2/

0



≤

≤

The directivity of the antenna is

(A) 10 dB

(B) 12.6 dB

(C) 11.5 dB

(D) 18 dB

Page 5

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

5/20

Q.18 If

][)2/1(

)3/1(][

nu

nx

n

n 



, then the region of convergence (ROC) of its Z-transform in the

Z-plane will be

(A)

3

3

1



z

(B)

2

1

3

1



z

(C)

3

2

1



z

(D)

z



3

1

Q.19 In the sum of products function

∑



)5,4,3,2(

),,(

ZYXf

, the prime implicants are

(A) YXYX

,

(B) ZYXZYXYX

,

,

(C) YXZYXZYX

,

,

(D) ZYXZYXZYXZYX

,

,

,

Q.20 A system with transfer function

)4()3()1(

)2()9

(

)(

2













s

s

s

s

s

sG

is excited by )(sint

. The steady-state output of the system is zero at

(A)

rad/s

1





(B)

rad/s

2





(C)

rad/s

3





(D)

rad/s

4





Q.21 The impedance looking into nodes 1 and 2 in the given circuit is

ib

99ib

9kΩ

100Ω

1kΩ

1

2

(A) 50 Ω

(B) 100 Ω

(C) 5 kΩ

(D) 10.1 kΩ

Q.22 In the circuit shown below, the current through the inductor is

1 Ω

1 Ω

j1 Ω

- j1 Ω

A

A

V

+

-

- +

V

1 0

1 0

1 0

1 0

(A)

A

1

2

j



(B)

A

1

1

j





(C)

A

1

1

j



(D) 0 A

Q.23 Given

3

2

1

1

)(









z

z

zf

. If C is a counterclockwise path in the z-plane such that

11





z

, the value of

∫C

dzzf

j

)(

2

1



is

(A) –2

(B) –1

(C) 1

(D) 2

Page 6

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

6/20

Q.24 Two independent random variables X and Y are uniformly distributed in the interval [–1, 1]. The

probability that max[X, Y] is less than 21 is

(A) 43

(B) 169

(C) 41

(D) 32

Q.25 If

1





x

, then the value of x

x is

(A)

2/





e

(B) 2/



e

(C) x

(D) 1

Q. 26 to Q. 55 carry two marks each.

Q.26 The source of a silicon (ni = 1010 per cm3) n-channel MOS transistor has an area of 1 sq µm and a

depth of 1 µm. If the dopant density in the source is 1019/cm3, the number of holes in the source

region with the above volume is approximately

(A) 107

(B) 100

(C) 10

(D) 0

Q.27 A BPSK scheme operating over an AWGN channel with noise power spectral density of

2

0

N

,

uses equiprobable signals

)(sin

2

)(

1

t

T

E

ts

c





and

)(sin

2

)(

2

t

T

E

ts

c







over the symbol

interval (0, T). If the local oscillator in a coherent receiver is ahead in phase by 45with respect to

the received signal, the probability of error in the resulting system is

(A)

│

│

⎠

⎞

│

│

⎝

⎛

0

2

N

E

Q

(B)

│

│

⎠

⎞

│

│

⎝

⎛

0

N

E

Q

(C)

│

│

⎠

⎞

│

│

⎝

⎛

0

2N

E

Q

(D)

│

│

⎠

⎞

│

│

⎝

⎛

0

4N

E

Q

Q.28 A transmission line with a characteristic impedance of 100 Ωis used to match a 50 Ωsection to a

200 Ωsection. If the matching is to be done both at 429 MHz and 1 GHz, the length of the

transmission line can be approximately

(A) 82.5 cm

(B) 1.05 m

(C) 1.58 m

(D) 1.75 m

Q.29 The input x(t) and output y(t) of a system are related as

∫

∞





t

d

x

ty





)3(cos)(

)(

. The system is

(A) time-invariant and stable

(B) stable and not time-invariant

(C) time-invariant and not stable

(D) not time-invariant and not stable

Q.30 The feedback system shown below oscillates at 2 rad/s when

R(s)

Y(s)

+

-

1

2

)1

(

2

3









s

as

s

sK

(A) K = 2 and a = 0.75

(B) K = 3 and a = 0.75

(C) K = 4 and a = 0.5

(D) K = 2 and a = 0.5

Q.31 The Fourier transform of a signal h(t) is









/)2(sin)

cos2()(



jH

. The value of h(0) is

(A) 1/4

(B) 1/2

(C) 1

(D) 2

Page 7

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

7/20

Q.32 The state variable description of an LTI system is given by

u

x

x

x

a

a

a

x

x

x

│

│

│

⎠

⎞

│

│

│

⎝

⎛



│

│

│

⎠

⎞

│

│

│

⎝

⎛

│

│

│

⎠

⎞

│

│

│

⎝

⎛



│

│

│

⎠

⎞

│

│

│

⎝

⎛

1

0

0

00

00

0

0

3

2

1

3

2

1

3

2

1

x

x

x





│

│

│

⎠

⎞

│

│

│

⎝

⎛



3

2

1

001

x

x

x

y

where y is the output and u is the input. The system is controllable for

(A)

0

1 ≠

a

,

0

2 

a

,

0

3 ≠

a

(B)

0

1 

a

,

0

2 ≠

a

,

0

3 ≠

a

(C)

0

1 

a

,

0

2 ≠

a

,

0

3 

a

(D)

0

1 ≠

a

,

0

2 ≠

a

,

0

3 

a

Q.33 Assuming both the voltage sources are in phase, the value of R for which maximum power is

transferred from circuit A to circuit B is

2 Ω

R

Circuit A

+

-

Circuit B

+

-

10 V

3 V

- j1 Ω

(A) 0.8 Ω

(B) 1.4 Ω

(C) 2 Ω

(D) 2.8 Ω

Q.34 Consider the differential equation

)(

)(

)(

2

)(

2

2

t

ty

dt

tdy

dt

tyd









with

2

)(

0







t

ty

and

0

0





t

dt

dy

.

The numerical value of



0

t

dt

dy

is

(A) –2

(B) –1

(C) 0

(D) 1

Q.35 The direction of vector A is radially outward from the origin, with

n

rk



A

where

2

2

2

2

z

y

x

r







and k is a constant. The value of n for which

0A



∙

∇

is

(A) –2

(B) 2

(C) 1

(D) 0

Q.36 A fair coin is tossed till a head appears for the first time. The probability that the number of

required tosses is odd, is

(A) 1/3

(B) 1/2

(C) 2/3

(D) 3/4

Page 8

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

8/20

Q.37 In the CMOS circuit shown, electron and hole mobilities are equal, and M1 and M2 are equally

sized. The device M1 is in the linear region if

Vin

|VTp|=1V

VTn=1V

5 V

M1

M2

(A) Vin < 1.875 V

(B) 1.875 V < Vin < 3.125 V

(C) Vin > 3.125 V

(D) 0 < Vin < 5 V

Q.38 A binary symmetric channel (BSC) has a transition probability of 1/8. If the binary transmit symbol

X is such that P(X=0) = 9/10, then the probability of error for an optimum receiver will be

(A) 7/80

(B) 63/80

(C) 9/10

(D) 1/10

Q.39 The signal m(t) as shown is applied both to a phase modulator (with p

k as the phase constant) and

a frequency modulator (with f

k as the frequency constant) having the same carrier frequency.

-2

m(t)

2

-2

t (seconds)

2

4

6

8

0

The ratio

f

p

kk (in rad/Hz) for the same maximum phase deviation is

(A) 8π

(B) 4π

(C) 2π

(D) π

Q.40 The magnetic field along the propagation direction inside a rectangular waveguide with the cross-

section shown in the figure is

)

10

283.6(cos)

10

618.2(cos)

10

094.2(cos3

10

2

2

z

t

y

x

Hz













X

Y

3 cm

1.2 cm

The phase velocity p

v of the wave inside the waveguide satisfies

(A)

c

vp 

(B)

c

vp 

(C)

c

vp 



0

(D)

0



p

v

Page 9

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

9/20

Q.41 The circuit shown is a

-

+

+

+

-

-

+5V

-5V

Input

Output

C

R1

R2

(A) low pass filter with f3dB =

CR

R

)

(

1

2

1 

rad/s

(B) high pass filter with f3dB =

CR1

1

rad/s

(C) low pass filter with f3dB =

CR1

1

rad/s

(D) high pass filter with f3dB =

CR

R

)

(

1

2

1 

rad/s

Q.42 Let y[n] denote the convolution of h[n] and g[n], where ][)2/1(][

nu

nh

n



and g[n] is a causal

sequence. If y[0] = 1 and y[1] = 1/2, then g[1] equals

(A) 0

(B) 1/2

(C) 1

(D) 3/2

Q.43 The state transition diagram for the logic circuit shown is

D

Q

CLK

Select

2-1 MUX

X1

X0

Y

A

Q

(A)

A=1

A=0

A=0

A=1

Q=1

Q=0

(B)

A=0

A=1

A=0

A=1

Q=1

Q=0

(C)

A=0

A=1

A=1

A=0

Q=1

Q=0

(D)

A=1

A=0

A=1

A=0

Q=1

Q=0

Page 10

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

10/20

Q.44 The voltage gain v

A of the circuit shown below is

vo

13.7 Volts

12kΩ

=100

100kΩ

10kΩ

vi

C

C

(A)

200

≈

v

A

(B)

100

≈

v

A

(C)

20

≈

v

A

(D)

10

≈

v

A

Q.45 If

V,6

V

V

B

A





then

D

C

V

V 

is

10 V

2 Ω

R

1 Ω

VA

VB

VC

VD

2 A

5 V

+ -

R

R

R

R

R

R

+

-

R

(A) –5 V

(B) 2 V

(C) 3 V

(D) 6 V

Q.46 The maximum value of

5

24

9

)(

2

3









x

x

x

xf

in the interval [1, 6] is

(A) 21

(B) 25

(C) 41

(D) 46

Q.47 Given that

│

⌋

⌉

│

⌊

⌈







0

2

3

5

A

and

,

10

01

│

⌋

⌉

│

⌊

⌈



I

the value of 3

A is

(A) 15 A + 12 I

(B) 19 A + 30 I

(C) 17 A + 15 I

(D) 17 A + 21 I

Page 11

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

11/20

Common Data Questions

Common Data for Questions 48 and 49:

With 10 V dc connected at port A in the linear nonreciprocal two-port network shown below, the following

were observed:

(i) 1 Ωconnected at port B draws a current of 3 A

(ii) 2.5 Ωconnected at port B draws a current of 2 A

+

-

A

B

Q.48 With 10 V dc connected at port A, the current drawn by 7 Ωconnected at port B is

(A) 3/7 A

(B) 5/7 A

(C) 1 A

(D) 9/7 A

Q.49 For the same network, with 6 V dc connected at port A, 1 Ωconnected at port B draws 7/3 A.

If 8 V dc is connected to port A, the open circuit voltage at port B is

(A) 6 V

(B) 7 V

(C) 8 V

(D) 9 V

Common Data for Questions 50 and 51:

In the three dimensional view of a silicon n-channel MOS transistor shown below, = 20 nm. The

transistor is of width 1 m. The depletion width formed at every p-n junction is 10 nm. The relative

permittivities of Si and SiO2, respectively, are 11.7 and 3.9, and 0 = 8.9 10-12 F/m.

G

D

S

B

0.2m

0.2m

0.2m

0.2m

m

1nm





D

m

p substrate

Q.50 The gate-source overlap capacitance is approximately

(A) 0.7 fF

(B) 0.7 pF

(C) 0.35 fF

(D) 0.24 pF

Q.51 The source-body junction capacitance is approximately

(A) 2 fF

(B) 7 fF

(C) 2 pF

(D) 7 pF

Page 12

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

12/20

Linked Answer Questions

Statement for Linked Answer Questions 52 and 53:

An infinitely long uniform solid wire of radius a carries a uniform dc current of density j

о

.

Q.52 The magnetic field at a distance r from the center of the wire is proportional to

(A) r for r < a and

2

1 r for r > a

(B) 0 for r < a and r

1 for r > a

(C) r for r < a and r

1 for r > a

(D) 0 for r < a and

2

1 r for r > a

Q.53 A hole of radius b (b < a) is now drilled along the length of the wire at a distance d from the center

of the wire as shown below.

a

b

d

The magnetic field inside the hole is

(A) uniform and depends only on d

(B) uniform and depends only on b

(C) uniform and depends on both b and d

(D) non uniform

Statement for Linked Answer Questions 54 and 55:

The transfer function of a compensator is given as

bs

as

sG

c







)(

.

Q.54

)(

sG

c

is a lead compensator if

(A) a =1, b = 2

(B) a = 3, b = 2

(C) a = –3, b = –1

(D) a = 3, b = 1

Q.55 The phase of the above lead compensator is maximum at

(A) 2 rad/s

(B) 3 rad/s

(C) 6 rad/s

(D) 3/1 rad/s

Page 13

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

13/20

General Aptitude (GA) Questions (Compulsory)

Q. 56 – Q. 60 carry one mark each.

Q.56 If (1.001)1259 = 3.52 and (1.001)2062 = 7.85, then (1.001)3321 =

(A) 2.23

(B) 4.33

(C) 11.37

(D) 27.64

Q.57 Choose the most appropriate alternative from the options given below to complete the following

sentence:

If the tired soldier wanted to lie down, he ___ the mattress out on the balcony.

(A) should take

(B) shall take

(C) should have taken

(D) will have taken

Q.58 Choose the most appropriate word from the options given below to complete the following

sentence:

Given the seriousness of the situation that he had to face, his ___ was impressive.

(A) beggary

(B) nomenclature

(C) jealousy

(D) nonchalance

Q.59 Which one of the following options is the closest in meaning to the word given below?

Latitude

(A) Eligibility

(B) Freedom

(C) Coercion

(D) Meticulousness

Q.60 One of the parts (A, B, C, D) in the sentence given below contains an ERROR. Which one of the

following is INCORRECT?

I requested that he should be given the driving test today instead of tomorrow.

(A) requested that

(B) should be given

(C) the driving test

(D) instead of tomorrow

Q. 61 - Q. 65 carry two marks each.

Q.61 One of the legacies of the Roman legions was discipline. In the legions, military law prevailed

and discipline was brutal. Discipline on the battlefield kept units obedient, intact and fighting,

even when the odds and conditions were against them.

Which one of the following statements best sums up the meaning of the above passage?

(A) Thorough regimentation was the main reason for the efficiency of the Roman legions even in

adverse circumstances.

(B) The legions were treated inhumanly as if the men were animals.

(C) Discipline was the armies’ inheritance from their seniors.

(D) The harsh discipline to which the legions were subjected to led to the odds and conditions being

against them.

Page 14

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

14/20

Q.62 Raju has 14 currency notes in his pocket consisting of only Rs. 20 notes and Rs. 10 notes. The total

money value of the notes is Rs. 230. The number of Rs. 10 notes that Raju has is

(A) 5

(B) 6

(C) 9

(D) 10

Q.63 There are eight bags of rice looking alike, seven of which have equal weight and one is slightly

heavier. The weighing balance is of unlimited capacity. Using this balance, the minimum number

of weighings required to identify the heavier bag is

(A) 2

(B) 3

(C) 4

(D) 8

Q.64 The data given in the following table summarizes the monthly budget of an average household.

Category

Amount (Rs.)

Food

4000

Clothing

1200

Rent

2000

Savings

1500

Other expenses

1800

The approximate percentage of the monthly budget NOT spent on savings is

(A) 10%

(B) 14%

(C) 81%

(D) 86%

Q.65 A and B are friends. They decide to meet between 1 PM and 2 PM on a given day. There is a

condition that whoever arrives first will not wait for the other for more than 15 minutes. The

probability that they will meet on that day is

(A) 1/4

(B) 1/16

(C) 7/16

(D) 9/16

END OF THE QUESTION PAPER

Page 15

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

15/20

Space for Rough Work

Page 16

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

16/20

Space for Rough Work

Page 17

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

17/20

Space for Rough Work

Page 18

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

18/20

Space for Rough Work

Page 19

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

19/20

Space for Rough Work

Page 20

2012

ELECTRONICS & COMMN. ENGG. - EC

EC-A

20/20

Space for Rough Work